## Slide 1: Week 3 Networking with the Pico W
Fundamentals of IoT
Dr. Eoin Rogers (eoin.rogers@tudublin.ie)

## Slide 2: Lesson Outline
Quick refresher on networking
Connecting the Pico to the Internet via wi-fi
Using the sockets API to send and receive data
Basic processing of the data using string/bytes manipulation functions/methods

## Slide 3: Networking
A quick refresher on modern computer networking

## Slide 4: Networking

## Slide 5: OSI networking model
Networks are structured as a series of layers
Each layer takes data from the layer above, packages it into a datagram format, and passes this to the layer below
There are two exceptions to this: the very topmost and bottommost layers:
  The physical layer represents hardware and passes raw bits on the physical network medium
  The application layer is expected to consume the data in some way

## Slide 6: TCP/IP and UDP/IP stacks

## Slide 7: Addressing
Each of these protocols have there own addressing schemes
Can anyone name the form of “address” used by:
  Ethernet
  WiFi
  IP
  TCP

## Slide 8: What happens when you type google.ie into your browser?

## Slide 9: What happens when you type google.ie into your browser?
A DNS lookup is performed to find the IP address
A HTTP request is created
The request is packaged into a TCP segment
The segment is packaged into an IP packet
The packet is packaged into a WiFi frame
The frame is transmitted over the network

## Slide 10: Connecting the Pico
The Pico W has a built-in WiFi chip

## Slide 11: Scanning for networks

## Slide 12: WiFi channels
WiFi uses radio configurations called channels. Unfortunately, the Pico only supports a subset of the channels that a typical laptop or phone would work with. In particular, it doesn't work with 5GHz channels, only the older 2.4GHz

## Slide 13: Connecting to a network

## Slide 14: Function to connect to WiFi

## Slide 15: A very basic “server”

## Slide 16: BSD sockets in Python
The only thing missing from the previous code snippet is using cxn.sendall() to send some raw Python bytes back to the client!
Link to tutorial

## Slide 17: Dealing with Python bytes
Python distinguishes between the str (string) and bytes datatype

## Slide 18: Dealing with bytes
Bytes-to-string: my_bytes.decode() (assumes UTF-8)
String-to-bytes: my_string.encode()
Bytes-to-int: each byte can be indexed into to get an integer, but are you sure you don’t want to convert to a string first?
Int-to-bytes: Create a list of integers in the range [0, 255], then pass it to bytes()

## Slide 19: Useful methods on strings and bytes
Slicing [x:y] (inclusive of x, exclusive of y)
.index(query) and .find(query) Find the index of the first instance of the query
.startswith(query) Returns true if the object starts with query
.endswith(query) Returns true if the object ends with query

## Slide 20: Summary
Went back over networking basics
How to scan for networks and connect to them on the Pico W using MicroPython
We can then use Python’s socket API (almost) the same way as in CPython
It’s important to understand how to use strings and bytes objects in Python effectively to work with these APIs

## Slide 21: 21
That’s all for this week
Thanks for your attention!